## Slide 1
Principles of Flight
- LIFT
Content copyrighted by Sunair Aviation Ltd.
The following content is in A4 size enabling the content to be printed easily.

## Slide 2
Bernoulli’s Theorem
“In the streamlined flow of an ideal fluid the sum of the static and dynamic
pressures remain a constant.”
Ps + PD = K
Venturi Effect Downwash / Newton’s 3rd Law
“For every action there is an equal and opposite reaction.”
Centre of Pressure
- A point where the summary of the total lift forces apply
- Roughly at 1/3 chord
Static pressure (Ps) = 5 = 2 = 5
Dynamic pressure (Pd) = 5 = 8 = 5
= 10 = 10 = 10
+
+
_
_
Lift is the force that opposes weight in level flight.
COP
PRODUCTION OF LIFT

## Slide 3
Camber
- Greater acceleration over top surface
- Greater difference in pressure
Angle of Attack
- Greater acceleration over top surface
- Build up of pressure under lower surface
- Greater difference in pressure
Airspeed
- Greater volume of airflow over wing
- Greater difference in pressure
L
L
L
L
L
L
+
_
+
_
+
_
+
_
+
_
+
_
FACTORS AFFECTING LIFT

## Slide 4
L = CL ½  V2 S
Aerofoil shape
Angle of attack
5A’s Air density
Airspeed
Area of wing
If any of the above factors increase, lift will increase.
D = CD  IAS  S
D = CD  IAS
Lift depends on Camber, AOA and IAS.
‘K’
LIFT FORMULA
Mathematical Velocity
Constant squared

## Slide 5
AOA
Aerofoils produce maximum lift just before the stall (16 approx).
After the stall, there is a significant drop in lift production.
High lift
GP
Symmetrical
CL
-4 0 16
CL max
LIFT CURVE

## Slide 6
A stall occurs when the critical angle of attack is exceeded. There is insufficient lift to maintain level flight.
4AOA 10AOA 15AOA
L
L
L
D
D
D
At 4 - COP acts 30% rearward from the L.E.
At 10 - COP acts 20% rearward from the L.E.
At 15 - COP acts 50% rearward from the L.E.
Before the stall - COP moves forward and is unstable.
After the stall - COP moves rearward and is stable.
STALLING

## Slide 7
Causes
Out of balance
- Crossed controls – Aileron use
Weight imbalance
- Roll – Aileron use
Ice/Damage
- Early flow separation
Turbulence
- Sudden change in AOA
- Roll – Aileron use
Flap
- Greater tendency to roll – Aileron use
Power
- Roll = Yaw – Aileron use
CL
CD
16
Critical angle
AOA
More drag Less drag
Use of Aileron
Down-going / Up-going wing
RAF
WING DROP STALL
One wing stalls before the other.

## Slide 8
Power W L AoA Vs
1043 1043 16⁰ 49kts
1043 900 16⁰ 45kts
Power = Vs
Flaps / Slats
Weight W L AoA Vs
900 900 16⁰ 45kts
1043 1043 16⁰ 49kts
W = Vs
Loading
Apparent weight = Vs
L = W + CFF
Loading = Vs
Ice / Damage / Contamination
Disturbs airflow = CL
Ice = W
= Vs
Negative factors / Increased stall speed Positive factors / Decreased stall speed
VCT
HCT
T
Flaps & slats
Plain wing
CL
16 AOA
VCT = 1043 - 900
= 143kg
L
W
CFF
FACTORS AFFECTING THE STALL

## Slide 9
Even lift
Trailing edge, more lift than leading edge.
COP 1/3 back from leading edge.
Envelope becomes larger, COP moves forward.
Envelope becomes even larger, COP moves forward.
Pressure envelope reaches its maximum, COP most forward position.
Pressure is reduced, COP moves rearward, lift is reduced.
-4
0
4
8
12
16
20
Summary
Up to 16AOA - COP moves forward and is unstable.
Beyond 16AOA - COP moves rearward and is stable.
The pressure distribution around the aerofoil vs AoA.
Pressure sensors
PRESSURE DISTRIBUTION