## Slide 1
Principles of Flight
- PERFORMANCE
Content copyrighted by Sunair Aviation Ltd.
The following content is in A4 size enabling the content to be printed easily.

## Slide 2
L = CL ½ V2 S
D = CD ½ V2 S
CL
CD

L
TR
D
Minimum 
= best L/D ratio
CL/CD
0 4 16 AOA
Stall
The lower the value of  the flatter the glide will be (best range).
LIFT / DRAG RATIO

## Slide 3
STRAIGHT & LEVEL
L = AOA x Airspeed
L
FCW
D
Lift
reduced
GLIDE DESCENT
W
T
4° AOA x 100kts
4° AOA x 65kts
W
W1
D
L
R
The speed for minimum drag normally occurs at 4 ⁰ AoA.
MINIMUM DRAG SPEED

## Slide 4
Characteristics
High CL max
- Low stall/landing speed
(agricultural aircraft)
High L/D ratio
- Maximum range
Low CD min
- High top speed
(streamlined)
Small C of P movement
- Lighter wing construction
(less structural stresses)
Sufficient depth
- Greater wing strength
(thicker spar)
CL
16 AOA
CL max
Stall
0 16 AOA
CD
minimum
CD
No such thing as the ideal aerofoil. Every design is a compromise.
IDEAL AEROFOIL

## Slide 5
50%
30%
Max thickness
Max thickness
CL
GP
Laminar flow
-4 0 16 AOA
LFA
GP
LFA
GP
Advantages Disadvantages
- Laminar flow lasts longer - Sensitive to surface condition
- Less skin friction drag at - Unpredictable stall characteristics
higher speeds - Higher stall speed
- Lower CL maximum
A LFA is a high speed, low drag aerofoil that is almost symmetrical.
LAMINAR FLOW AEROFOIL

## Slide 6
Flying for range is travelling the greatest distance on a given amount of fuel.
4 AOA IAS
Min drag
Total Drag
Stall
Best range TAS
PR
Factors affecting range
Fuel - More fuel = greater range
Speed - Higher GS = greater range
Drag – Less drag = less fuel burn =
greater range
‘K’
W = F x D
W = Fuel onboard
F = Drag
Maximise distance by flying at min drag speed.
PR = Drag x TAS
Maximise range by flying at highest TAS vs PR ratio.
Considerations
Weight - Heavier = more power/higher IAS
Engine - Low RPM & high manifold pressure
- Mixture as lean as possible
Airframe - Clean Best L/D ratio
Wind - Tailwind Higher GS
Altitude - No effect however best at FTH
- PR and TAS both increase
C of G - Rearward Reduces negative lift from tailplane
Headwind
Nil wind
Tailwind
FLYING FOR RANGE (PISTON)

## Slide 7
Best range IAS
(Nil wind)
Considerations
Weight - Heavier = more thrust/higher IAS
Airframe - Clean
Wind - Tailwind Higher GS
Altitude - Higher Constant thrust, higher TAS
C of G - Rearward Reduces negative lift from tailplane
Flying for range is travelling the greatest distance on a given amount of fuel.
FLYING FOR RANGE (TURBINE)
Total Drag / TR
Factors affecting range
Fuel - More fuel = greater range
Speed - Higher GS = greater range
Drag – Less drag = less fuel burn =
greater range
‘K’
W = F x D
W = Fuel onboard
F = Drag
Maximise distance by flying at min drag vs speed ratio.
Note: This is different to propeller aircraft since turbofan/jet engines operate better at higher speed.

## Slide 8
Factors affecting endurance
Fuel
- More fuel = longer flight time
Consumption rate
- Less fuel burn = greater endurance
‘K’
W = P x T
P = Power
T = Time taken
Minimum power setting = minimum fuel consumption rate.
Considerations
Engine - RPM, mixture as per flight manual
Airframe - Clean configuration
Altitude - Low as possible
Weight - Low weight
Wind - No effect
C of G - Rearward is better
PR
Maximum
endurance
Minimum
power
TAS
Flying for endurance is flying for the longest possible time on a given amount of fuel.
FLYING FOR ENDURANCE (PISTON)

## Slide 9
Factors affecting endurance
Fuel
- More fuel = longer flight time
Consumption rate
- Less fuel burn = greater endurance
Drag = Thrust required
Minimum drag equals minimum thrust required, i.e. minimum fuel consumption rate.
Note: Turbofan/jet aircraft best endurance is similar speed to propeller aircraft best range.
Considerations
Airframe - Clean configuration
Altitude - No effect
Weight - Low weight
Wind - No effect
C of G - Rearward is better
Total Drag / TR
Maximum
endurance
Minimum
thrust
IAS
Flying for endurance is flying for the longest possible time on a given amount of fuel.
FLYING FOR ENDURANCE (TURBINE)

## Slide 10
Power
TAS
PA
PR
Min
speed
Max
speed
Factors affecting speed range
Weight = PR = Speed range
Drag = PR = Speed range
Altitude = PR - PA = Speed range
‘K’
Lift = AOA  IAS,
PR = Drag  TAS
‘K’
PR = Drag  TAS
‘K’
PR = Drag  TAS
Stall
The range of speeds we can fly the aircraft in straight and level.
SPEED RANGE

## Slide 11
ENGINE PERFORMANCE
Combustion
- Full rich gives high fuel flow
- Correct ratio → best performance
- Mixture is leaned as air density reduces
- Engine power is affected by air density
Air Pressure
- Higher pressure,
greater density
Air Temperature
- Lower temperature, greater density
WING / PROP PERFORMANCE
Lift = AoA x IAS
- IAS reduces while TAS remains
constant – Lift reduces
↑ PR = Drag x ↑ TAS
- To keep IAS (Lift) constant, TAS &
power must be increased
ISA - International Standard Atmosphere
At Mean Sea Level: Pressure - 1013.25 hPa, temperature - 15C, Air density – 1.225 kg/m³
TAKEOFF / LANDING CONSIDERATIONS
Weight
- More weight → Slower acceleration,
shallower climb angle
- Slower deceleration
Wind
- Headwind → Steep climb/descent angle
- Tailwind → Shallow climb/descent angle
Surface
- Soft surface → slow acceleration
- Less braking action
Slope
- Up slope → Slow acceleration/fast
deceleration
- Down slope → Fast acceleration/slow
deceleration
100kts IAS
100kts TAS
80kts IAS
100kts TAS
Cold Air – More Dense
Warm Air – Less Dense
Sea Level
10,000ft
‘K’
Thrust 100kts TAS
100kts IAS
80kts IAS
FACTORS AFFECTING PERFORMANCE