## Slide 1
Principles of Flight
- PROPELLERS
Content copyrighted by Sunair Aviation Ltd.
The following content is in A4 size enabling the content to be printed easily.

## Slide 2
Direction
of travel
+4 0 -4
Actual pitch
Geometric pitch
Experimental mean pitch (EMP)
TR
T
Prop Torque
Plane of rotation
Helix
Angle
AOA
Blade Angle
RAF
Chord line
Line of zero thrust
Angle of Attack
- Angle between RAF and chord line
Helix Angle
- Angle between plane of rotation and RAF
Blade Angle
- Angle between plane of rotation and Chord line
Actual Pitch
- Distance travelled by prop in one rotation
Geometric Pitch
- Distance travelled by prop in one rotation at 0 AOA
Experimental Mean Pitch
- Distance travelled by prop in one rotation at zero thrust
Slip
- Distance between Actual pitch and EMP, most
efficient at 30% slip
100% Slip
- Full power, brakes on = No forward movement
= No work done
0% Slip
- Glide, large distance travelled, no thrust = No work done
Slip
Thrust is the force that opposes drag in level flight.
THRUST

## Slide 3
70%
Blade length %
100%
Greatest lift produced at 70% (approx) from hub.
Direction
of travel
Plane of
rotation
TR
TR
The TR of the outer blade section is more tilted inline with the direction of travel.
PRODUCTION OF LIFT ON A BLADE

## Slide 4
Forward velocity in ½ a revolution
Propeller twist ensures a constant AOA is maintained over the blade.
RAF
RAF
Propeller twist is a reduction in blade angle from root to tip.
PROPELLER TWIST

## Slide 5
Constant speed units are used to allow pitch to change as speed changes.
The CSU ensures that constant AOA is maintained over a range of speeds.
Constant
RPM
Fine Coarse
TAS
RAF
RAF
Slow
Fast
Efficiency
TAS
Coarse pitch limit
Fine pitch limit
Peak efficiency
VARIABLE PITCH PROPELLER

## Slide 6
Solidity =
Blade Area
Area of Air
Ways of increasing Solidity
Chord = blade area
Aspect Ratio
No. of Blades = blade area
Cost of manufacture, blade interference
Other ways of increasing power absorption
Camber = TR and prop torque
Efficiency
RPM = Drag and prop torque
Tip speed
Blade length = Larger disc area, prop torque
Tip speed
Blade angle = AOA and prop torque
Efficiency
Solidity is a measure of the propellers ability to absorb engine power.
POWER ABSORPTION

## Slide 7
CFF CFF
CTM CTM
Pitch change
axis
CFF acting on the blade originates from the centre of rotation.
Increasing blade width or RPM results in an increase in CTM.
CTM acts to Fine the blade.
Pitch change
axis
CENTRIFUGAL TWISTING MOMENT

## Slide 8
Normal flight
Windmilling
TR
RAF
Plane of rotation
Pitch change axis
Direction of travel
TR
Pitch change axis
RAF
Plane of rotation
Under normal flight conditions ATM acts to Coarsen the blade.
Under windmilling flight conditions ATM and CTM both act to Fine the blade.
Direction of travel
ATM occurs when the TR does not act through the pitch change axis
AERODYNAMIC TWISTING MOMENT

## Slide 9
TAS
L
TR
D
T
Prop torque
Rotational velocity
Cruise
Windmilling
Reverse thrust
(power-on brake)
TAS
TAS
TR
Windmilling drag
Prop torque
Rotational velocity
TR
T
Prop torque
Rotational velocity
Propeller torque acts in the same direction as engine torque.
Reverse thrust acts opposite to the direction of travel.
FORCES ON A PROPELLER BLADE