## Slide 1
Straight and Level
Briefing copyrighted by Sunair Aviation Ltd.

## Slide 2
Objectives
To establish and maintain straight and level flight, at a constant airspeed, altitude, direction and in balance
To regain straight and level flight
To maintain straight and level flight at selected airspeeds or power settings

## Slide 3
Principles of Flight
Horizon
In VFR flight, straight and level is accomplished with reference to the horizon
Weather or terrain can hide the actual horizon
Artificial horizon may be used where no actual horizon exists
-
-
-

## Slide 4
Forces in Straight & Level
Equilibrium: Constant direction and airspeed
Weight
Lift
Thrust
Drag
W
L
T
D
Tail plane and elevator provide
pitch balancing moment
T/D Couple
L/W Couple
L = W T = D
Principles of Flight

## Slide 5
Lift Formula
Camber
Angle of Attack
Indicated Airspeed
Wing Surface Area
L = Angle of Attack x Airspeed
Power + Attitude = Performance
½  V2
CL
S
L =
Principles of Flight

## Slide 6
Throttle
Recommended cruise 2200rpm
Smooth, positive throttle movements
Mixture
Full rich for training
Lean at altitude
Idle-cut-off
Carb Heat
Hot below rpm green range
Fuel Management
(fuel drains, unusable/usable fuel)
SCADIE Check
Aircraft Management
-
-
-
-
-
-

## Slide 7
Suction - Green range (4.5 – 5.4 in.Hg.)
Carbon monoxide
Ammeter - Zero or positive charge
D.I. - Direction Indicator aligned with magnetic compass
Icing - Cycle carb heat
Engine - Oil temperature and Pressure (T’s & P’s)
Aircraft Management

## Slide 8
VFR Met Minima
Uncontrolled aerodromes
600ft cloud ceiling
1500m visibility
Uncontrolled airspace 3000ft AMSL
Clear of cloud
In sight of the surface
5km visibility
Orientation
Local landmarks
Aircraft Management
-
-
-
-
-
-

## Slide 9
Lookout
Blindspots
Sectored scan (2 sec per 20 degrees)
Situational Awareness
Other traffic, weather, terrain
Airmanship
I have You have control
Training area boundaries
Blind spots
Human Factors
-
-
-
-
-
IM SAFE

## Slide 10
Reference
Select reference point
Select reference altitude
Configuration
2200rpm
Note nose attitude relative to the horizon
Wings level
Balance ball centralised
Aircraft trimmed for S&L attitude
Airspeed approximately 100kts
Establishing S&L
Power – Set cruise power
Attitude – Visually set and hold nose attitude
Trim – Relieve control column pressure
Maintain
Lookout – Traffic, Cloud, Terrain
Attitude – Check nose attitude and reference point
Instruments – Quick glance to confirm altitude, balance, and speed
Air Exercise
-
-
-
-
-
-
-
-
Last Slide

## Slide 11
Power + Attitude = Performance
Demonstration
Straight and Level flight at different power settings and configurations
Air Exercise
-
Last Slide